# Messenger send test results

The performance of messenger send has been tested using the cbench:c test program. The cbench:c program operates in two modes latency and throughput. Results shown below are throughput output results. This document should be used in conjunction with the messenger send design document. Each test has some preconditions that we list and set appropriate before testing commences. Some of these preconditions are conditional code that needs to be compiled and enabled. The following is a list of messenger's send conditional flags:
- MCAS multiple compare and store not set by default. CAS is enabled by default.
- MUTEX exclusive locking an unlocking not set by default. Ticket locking algorithm enabled by default.
- BLOOM reference code only. At it is would not work even if enabled.
- PARTITION splits job queue computation into two halves not enabled by default. Default is one message for each send call.
## Environment setup fixed parameters
Certain parameters that affect the performance of messenger is the number of tasks and the size of job queue size.
For all tests the number of tasks set to 2 and the job queue size set to 512 items before queue becomes full.
All tests conducted in two separate environments the specifications of each shown below.
Environment#0
Processor : 0 / cpu MHz : 2666.896 / cache size : 4096 KB
Environment#1
processor : 0 / cpu MHz : 2000.000 / cache size : 6144 KB / processor : 1 / cpu MHz : 2000.000 / cache size : 6144 KB / processor : 2 / cpu MHz : 2000.000 / cache size : 6144 KB / processor : 3 / cpu MHz : 2000.000 / cache size : 6144 KB

We run all the tests twice and pick the best results among them. If during the test the job queue becomes full we confirm this by searching for a specific queue full message in the output log files.

## Test cases

### Original version
### Results
#### Environment#0
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/home/nick/develop-origin/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 68904 total = 68.821002 per ms
1 switches: fmods/sec: 69806 total = 69.791274 per ms
1 switches: fmods/sec: 70324 total = 69.876164 per ms
1 switches: fmods/sec: 68764 total = 68.737261 per ms
1 switches: fmods/sec: 70651 total = 69.748042 per ms
1 switches: fmods/sec: 65474 total = 65.345987 per ms
1 switches: fmods/sec: 64108 total = 64.098321 per ms
1 switches: fmods/sec: 62734 total = 62.599036 per ms
1 switches: fmods/sec: 63735 total = 63.447582 per ms
1 switches: fmods/sec: 65629 total = 65.448624 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 62599.04/69876.16/66565.81/2798.55 responses/s

No messages discarded due to overflow.
#### Environment#1
Unable to obtained results cbench:c always aborted with error.

### Case # 1

#### Preconditions

The following preconditions are set and valid during the test
- conditional compilation with MCAS flag (multiple compare and swap) in add_job().
- Mutex exclusive locking is used conditional compilation with MUTEX flag.

1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 36 / 37 / 38 / 39 / 40 / 41 / 42	static bool / add_job( job_ctrl *ctrl, job_item *item ) { / job_item *rear_item; / int rear; / int tmp; / if ( job_queue_full( ctrl ) ) { / return 0; / } / while ( true ) { / rear = ctrl->rear; / tmp = ( rear + 1 ) % ITEM_ARRAY_SIZE; / if ( rear != ctrl->rear ) { / continue; / } / rear_item = &ctrl->item[ rear ]; / #ifdef MCAS / if ( MCAS( ( int * ) &ctrl->item[ rear ], ( int * ) rear_item, ( int * ) item, sizeof( *item ) ) ) { / #else / if ( CAS( ( int * ) &ctrl->item[ rear ], ( int * ) rear_item, ( int * ) item, sizeof( *item ) ) ) { / #endif / CAS_int( &ctrl->rear, rear, tmp ); / return 1; / } / } / }

#### Results
##### Environment#0
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/home/nick/test_develop/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 30217 total = 29.924725 per ms
1 switches: fmods/sec: 30322 total = 30.309664 per ms
1 switches: fmods/sec: 29261 total = 29.196184 per ms
1 switches: fmods/sec: 28278 total = 28.276134 per ms
1 switches: fmods/sec: 28527 total = 28.319840 per ms
1 switches: fmods/sec: 28225 total = 28.205933 per ms
1 switches: fmods/sec: 27519 total = 27.357672 per ms
1 switches: fmods/sec: 28521 total = 28.296917 per ms
1 switches: fmods/sec: 28452 total = 28.295948 per ms
1 switches: fmods/sec: 28105 total = 27.874008 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 27357.67/30309.66/28459.14/795.35 responses/s

##### Environment#1
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/host/Users/co2kara/Documents/projects/trema/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 54138 total = 54.090130 per ms
1 switches: fmods/sec: 56016 total = 55.921158 per ms
1 switches: fmods/sec: 67927 total = 67.729298 per ms
1 switches: fmods/sec: 64312 total = 64.177036 per ms
1 switches: fmods/sec: 66948 total = 66.813104 per ms
1 switches: fmods/sec: 64163 total = 64.074769 per ms
1 switches: fmods/sec: 63290 total = 63.144326 per ms
1 switches: fmods/sec: 62662 total = 62.588959 per ms
1 switches: fmods/sec: 61386 total = 61.248742 per ms
1 switches: fmods/sec: 61359 total = 61.307869 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 55921.16/67729.30/63000.58/3260.48 responses/s

#### Job queue status
##### Environment#0
grep -c "queue is full" *.log
cbench_switch.log:0
switch.0x1.log:0
switch_manager.log:0
No message discarded due to queue full.
##### Environment#1
grep -c "queue is full" *
cbench_switch.log:4
switch.0x1.log:6
switch.127.0.0.1:42177.log:0
switch.127.0.0.1:56264.log:0
switch_manager.log:0
10 messages discarded due to queue full.

### Case #2

#### Preconditions
The following preconditions set and valid during the test.
- Use CAS function in add_job() default compilation. CAS uses memcmp and memcpy.
- Mutex exclusive locking is used conditional compilation with MUTEX flag.

1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 36 / 37 / 38 / 39 / 40 / 41 / 42	static bool / add_job( job_ctrl *ctrl, job_item *item ) { / job_item *rear_item; / int rear; / int tmp; / if ( job_queue_full( ctrl ) ) { / return 0; / } / while ( true ) { / rear = ctrl->rear; / tmp = ( rear + 1 ) % ITEM_ARRAY_SIZE; / if ( rear != ctrl->rear ) { / continue; / } / rear_item = &ctrl->item[ rear ]; / #ifdef MCAS / if ( MCAS( ( int * ) &ctrl->item[ rear ], ( int * ) rear_item, ( int * ) item, sizeof( *item ) ) ) { / #else / if ( CAS( ( int * ) &ctrl->item[ rear ], ( int * ) rear_item, ( int * ) item, sizeof( *item ) ) ) { / #endif / CAS_int( &ctrl->rear, rear, tmp ); / return 1; / } / } / }

#### Results
##### Environment#0
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/home/nick/test_develop/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 29685 total = 29.423513 per ms
1 switches: fmods/sec: 28573 total = 28.445422 per ms
1 switches: fmods/sec: 28083 total = 27.728135 per ms
1 switches: fmods/sec: 29113 total = 28.802651 per ms
1 switches: fmods/sec: 28955 total = 28.625718 per ms
1 switches: fmods/sec: 28644 total = 28.640076 per ms
1 switches: fmods/sec: 28682 total = 28.469278 per ms
1 switches: fmods/sec: 28344 total = 28.298496 per ms
1 switches: fmods/sec: 28202 total = 28.191315 per ms
1 switches: fmods/sec: 28174 total = 28.006911 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 27728.14/28802.65/28356.44/319.77 responses/s

##### Environment#1
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/host/Users/co2kara/Documents/projects/trema/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 70396 total = 70.232639 per ms
1 switches: fmods/sec: 69185 total = 69.168123 per ms
1 switches: fmods/sec: 68717 total = 68.565812 per ms
1 switches: fmods/sec: 68063 total = 67.865714 per ms
1 switches: fmods/sec: 66984 total = 66.842094 per ms
1 switches: fmods/sec: 65743 total = 65.500256 per ms
1 switches: fmods/sec: 66101 total = 65.999625 per ms
1 switches: fmods/sec: 64689 total = 64.678845 per ms
1 switches: fmods/sec: 64290 total = 64.221604 per ms
1 switches: fmods/sec: 63497 total = 63.355527 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 63355.53/69168.12/66244.18/1898.10 responses/s

#### Job queue status
##### Environment#0
grep -c "queue is full" *.log
cbench_switch.log:0
switch.0x1.log:0
switch_manager.log:0
No message discarded due to queue full.
##### Environment#1
grep -c "queue is full" *
cbench_switch.log:1
switch.0x1.log:0
switch.127.0.0.1:42177.log:0
switch.127.0.0.1:56264.log:0
switch_manager.log:0
1 message discarded due to queue full.

### Case #3

#### Preconditions
The following preconditions set and valid during the test.
- conditional compilation with MCAS flag (multiple compare and swap) in add_job().
- Job queue size partitioned in halve conditional compilation with PARTITION flag.
- Mutex exclusive locking is used conditional compilation with MUTEX flag.

1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 35 / 37 / 38 / 39	static void / exec_partition( job_ctrl *ctrl ) { / int ret = 1; / job_item *item; / struct timespec req; / int front; / int tmp; / int rear; / int thread_idx = 1; / if ( ctrl->tid[ 1 ] == self() ) { / thread_idx = 2; / } / int min = ( thread_idx - 1 ) * 256; / int max = thread_idx * 256; / req.tv_sec = 0; / while ( true ) { / front = ctrl->front; / rear = ctrl->rear; / if ( front == rear ) { / req.tv_nsec = 1; / nanosleep( &req, NULL ); / continue; / } / front = ctrl->front; / if ( front >= min && front < max ) { / item = &ctrl->item[ front ]; / tmp = ( front + 1 ) % ITEM_ARRAY_SIZE; / ctrl->front = tmp; / send( item->opt.server_socket, item->opt.buffer, item->opt.buffer_len, MSG_DONTWAIT ); / } / else { / req.tv_nsec = 10; / nanosleep( &req, NULL ); / } / } / }

#### Results
##### Environment#0
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/home/nick/test_develop/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 28647 total = 28.320605 per ms
1 switches: fmods/sec: 28443 total = 28.355721 per ms
1 switches: fmods/sec: 29291 total = 29.233965 per ms
1 switches: fmods/sec: 29510 total = 29.126894 per ms
1 switches: fmods/sec: 28594 total = 28.214654 per ms
1 switches: fmods/sec: 28571 total = 28.217436 per ms
1 switches: fmods/sec: 28300 total = 28.148365 per ms
1 switches: fmods/sec: 27942 total = 27.760392 per ms
1 switches: fmods/sec: 27631 total = 27.625005 per ms
1 switches: fmods/sec: 27245 total = 27.031237 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 27031.24/29233.96/28190.41/653.60 responses/s

##### Environment#1
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/host/Users/co2kara/Documents/projects/trema/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 54377 total = 54.359605 per ms
1 switches: fmods/sec: 68467 total = 68.407964 per ms
1 switches: fmods/sec: 58672 total = 58.590091 per ms
1 switches: fmods/sec: 58338 total = 58.112408 per ms
1 switches: fmods/sec: 63797 total = 63.591726 per ms
1 switches: fmods/sec: 66610 total = 66.583699 per ms
1 switches: fmods/sec: 60711 total = 60.616559 per ms
1 switches: fmods/sec: 61422 total = 61.224978 per ms
1 switches: fmods/sec: 59225 total = 59.032672 per ms
1 switches: fmods/sec: 56878 total = 56.629904 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 56629.90/68407.96/61421.11/3778.42 responses/s

#### Job queue status
##### Environment#0
grep -c "queue is full" *.log
cbench_switch.log:0
switch.0x1.log:0
switch_manager.log:0
No message discarded due to queue full.
##### Environment#1
grep -c "queue is full" *.log
cbench_switch.log:0
switch.0x1.log:0
switch_manager.log:0
No message discarded due to queue full.
### Case #4

#### Preconditions
The following preconditions set and valid during the test.
- Use CAS function in add_job() default compilation. CAS uses memcmp and memcpy.
- Job queue size partitioned in halve conditional compilation with PARTITION flag.
- Mutex exclusive locking is used conditional compilation with MUTEX flag.

#### Results
##### Environment#0
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/home/nick/test_develop/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 30175 total = 29.969708 per ms
1 switches: fmods/sec: 30234 total = 29.969697 per ms
1 switches: fmods/sec: 29279 total = 29.228785 per ms
1 switches: fmods/sec: 28245 total = 28.145029 per ms
1 switches: fmods/sec: 28829 total = 28.514175 per ms
1 switches: fmods/sec: 29193 total = 28.860955 per ms
1 switches: fmods/sec: 28563 total = 28.558374 per ms
1 switches: fmods/sec: 28240 total = 27.940340 per ms
1 switches: fmods/sec: 28216 total = 28.046292 per ms
1 switches: fmods/sec: 27516 total = 27.474760 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 27474.76/29969.70/28526.49/708.28 responses/s

##### Environment#1
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/host/Users/co2kara/Documents/projects/trema/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 70552 total = 70.331160 per ms
1 switches: fmods/sec: 68288 total = 68.270181 per ms
1 switches: fmods/sec: 67782 total = 67.750970 per ms
1 switches: fmods/sec: 67736 total = 67.553268 per ms
1 switches: fmods/sec: 66131 total = 65.894702 per ms
1 switches: fmods/sec: 65091 total = 65.065689 per ms
1 switches: fmods/sec: 63953 total = 63.872967 per ms
1 switches: fmods/sec: 63741 total = 63.538883 per ms
1 switches: fmods/sec: 63118 total = 62.952247 per ms
1 switches: fmods/sec: 62615 total = 62.429148 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 62429.15/68270.18/65258.67/2086.77 responses/s

#### Job queue status
##### Environment#0
grep -c "queue is full" *.log
cbench_switch.log:0
switch.0x1.log:0
switch_manager.log:0
No message discarded due to queue full.
##### Environment#1
grep -c "queue is full" *.log
cbench_switch.log:0
switch.0x1.log:0
switch_manager.log:0
No message discarded due to queue full.
### Case #5

#### Preconditions
The following preconditions set and valid during the test.
- Use CAS function in add_job() default compilation. CAS uses memcmp and memcpy.
- Ticket locking algorithm enabled default compilation.

#### Results
##### Environment#0
./trema killall
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/home/nick/test_develop/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 31056 total = 31.012459 per ms
1 switches: fmods/sec: 31814 total = 31.734315 per ms
1 switches: fmods/sec: 26021 total = 25.970254 per ms
1 switches: fmods/sec: 30223 total = 29.944872 per ms
1 switches: fmods/sec: 29910 total = 29.825028 per ms
1 switches: fmods/sec: 29604 total = 29.537069 per ms
1 switches: fmods/sec: 29358 total = 29.049236 per ms
1 switches: fmods/sec: 28847 total = 28.810353 per ms
1 switches: fmods/sec: 28732 total = 28.532076 per ms
1 switches: fmods/sec: 27413 total = 27.025748 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 25970.25/31734.32/28936.55/1585.93 responses/

##### Environment#1
./trema run ./objects/examples/cbench_switch/cbench_switch -d
/host/Users/co2kara/Documents/projects/trema/objects/oflops/bin/cbench --switches 1 --loops 10 --delay 1000 --throughput
cbench: controller benchmarking tool
   running in mode 'throughput'
   connecting to controller at localhost:6633
   faking 1 switches :: 10 tests each; 1000 ms per test
   with 100000 unique source MACs per switch
   starting test with 1000 ms delay after features_reply
   ignoring first 1 "warmup" and last 0 "cooldown" loops
   debugging info is off
1 switches: fmods/sec: 65952 total = 65.865650 per ms
1 switches: fmods/sec: 68135 total = 67.961359 per ms
1 switches: fmods/sec: 49442 total = 49.380620 per ms
1 switches: fmods/sec: 63623 total = 63.503486 per ms
1 switches: fmods/sec: 64708 total = 64.566470 per ms
1 switches: fmods/sec: 64793 total = 64.563413 per ms
1 switches: fmods/sec: 62270 total = 62.078735 per ms
1 switches: fmods/sec: 65073 total = 65.044836 per ms
1 switches: fmods/sec: 63793 total = 63.505321 per ms
1 switches: fmods/sec: 64182 total = 64.165189 per ms
RESULT: 1 switches 9 tests min/max/avg/stdev = 49380.62/67961.36/62752.16/4959.22 responses/s

#### Job queue status
##### Environment#0
grep -c "queue is full" *.log
cbench_switch.log:0
switch.0x1.log:0
switch_manager.log:0
No message discarded due to queue full.
##### Environment#1
grep -c "queue is full" *
cbench_switch.log:9
switch.0x1.log:9
switch.127.0.0.1:42177.log:0
switch.127.0.0.1:56264.log:0
switch_manager.log:0
18 messages loss due to queue full.

## Graphical representation of results

For both environments for all test cases a graphical representation of the results shown below.

messenger send performance
environment#0

messenger send performance
environment#1